## Slide 1
5G PCAP Parsing
Methods · Results · Why We Chose pyshark
Unified Telecom Analyzer | Reviewer Briefing | 2026
3GPP TS 24.501 · 38.413 · 38.331 · 38.473 · 38.463 · 38.423

## Slide 2
Agenda
01
What is PCAP and why does 5G parsing matter?
02
4 Parsing Methods — Overview
03
Method 1: pyshark (Wireshark wrapper)
04
Method 2: scapy (Raw packet crafting)
05
Method 3: dpkt (Lightweight C bindings)
06
Method 4: asn1tools (Pure ASN.1 decoder)
07
Head-to-head Comparison Table
08
Why we chose pyshark — Decision Rationale
09
Live Result Demo — Dashboard

## Slide 3
What is PCAP — and why is 5G parsing hard?
PCAP (Packet Capture)
• Network traffic captured at wire level
• Contains Ethernet → IP → UDP/SCTP → App layers
• Standard format: .pcap / .pcapng
• Tool: tcpdump, Wireshark, tshark
In 5G networks, the application layer carries:
NAS, NGAP, RRC, F1AP, E1AP, XnAP
These are encoded in binary ASN.1 / 3GPP custom
format — NOT plain text, NOT HTTP/JSON.
5G Protocol Stack in a PCAP
NAS (TS 24.501)
5GMM + 5GSM — UE ↔ Core
NGAP (TS 38.413)
N2 interface — gNB ↔ AMF
RRC (TS 38.331)
Uu interface — UE ↔ gNB
F1AP (TS 38.473)
F1 interface — DU ↔ CU-CP
E1AP (TS 38.463)
E1 interface — CU-CP ↔ CU-UP
XnAP (TS 38.423)
Xn interface — gNB ↔ gNB

## Slide 4
4 Approaches to 5G PCAP Parsing
01
pyshark
Wireshark wrapper
Full 3GPP dissectors built-in
02
scapy
Raw packet crafting
IP/UDP only — 5G: manual bytes
03
dpkt
C-speed bindings
Transport layer only
04
asn1tools
Pure ASN.1 decoder
Spec-accurate but very complex setup
We evaluated all four before selecting the method for this project.

## Slide 5
01
pyshark
Wireshark / tshark wrapper — full 3GPP dissector stack
python
import pyshark
cap = pyshark.FileCapture('test.pcap',
display_filter='ngap or nas-5gs')
for pkt in cap:
proc = pkt.ngap.procedurecode
cause = pkt.nas_5gs.mm.cause
print(proc, cause) # decoded field names
✅ Pros
• Full NAS/NGAP/RRC/F1AP/E1AP/XnAP
• Real 3GPP field names
• IE extraction built-in
• 20-year community tested
• Low setup (just tshark)
❌ Cons
• Slow (spawns tshark process)
• Requires tshark installed
• Not pure Python
Actual Results
✅ NAS decoded: Registration, Auth,
SecurityMode, PDU Session,
Deregistration
✅ NGAP decoded: InitialContextSetup,
PDUSessionResourceSetup,
UEContextRelease, Handover
✅ F1AP / E1AP / XnAP: all procedures
with cause IEs extracted
✅ Dashboard: 6 protocol tabs,
IE inspector, failure cause
breakdown — all working

## Slide 6
02
scapy
Raw packet crafting library — IP/UDP, no 5G protocol awareness
python
from scapy.all import rdpcap
pkts = rdpcap('test.pcap')
for pkt in pkts:
if pkt.haslayer('UDP'):
raw = bytes(pkt['UDP'].payload)
# raw = b'\x7e\x00\x41...'
# Must parse 5G manually
✅ Pros
• Fast, pure Python
• Ethernet/IP/UDP/SCTP fine
• Good packet crafting
• No external tools needed
❌ Cons
• No 5G protocol support
• Raw bytes only for NAS/NGAP
• Manual TLV/ASN.1 needed
• ~3000 lines to replicate pyshark
Actual Results
❌ NAS: raw bytes b'\x7e\x00...'
No procedure name
No IE extraction
❌ NGAP: b'\x00\x15\x00...'
ASN.1 PER — unreadable
without custom decoder
❌ F1AP / E1AP / XnAP: same issue
✅ IP/UDP headers: src/dst IP,
ports, timestamps — fine
Verdict: usable as fallback for
raw discriminator matching only

## Slide 7
03
dpkt
Lightweight C bindings — transport layer only, maximum speed
python
import dpkt
with open('test.pcap', 'rb') as f:
pcap = dpkt.pcap.Reader(f)
for ts, buf in pcap:
eth = dpkt.ethernet.Ethernet(buf)
payload = eth.ip.udp.data
# payload = raw 5G bytes, no decode
✅ Pros
• Fastest parser (C bindings)
• Minimal memory usage
• Ethernet/IP/TCP/UDP/SCTP
• No dependencies
❌ Cons
• Zero 5G protocol awareness
• No application layer decode
• More limited than scapy
• No active development
Actual Results
❌ 5G protocols: completely opaque
bytes after UDP layer
❌ No NAS/NGAP/RRC/F1AP/E1AP/XnAP
✅ Transport metadata only:
timestamps, src/dst IP,
packet sizes, flow info
Use case: high-speed packet
counting / flow statistics only.
Not suitable for 5G signaling
analysis at all.
Verdict: eliminated early.

## Slide 8
04
asn1tools
Pure ASN.1 decoder — spec-accurate but complex setup
python
import asn1tools
# Need .asn schema file per protocol
ngap = asn1tools.compile_files(
['NGAP-PDU-Descriptions.asn',
'NGAP-IEs.asn', ...])
decoded = ngap.decode('NGAP-PDU', raw)
# NAS: custom TLV — asn1tools can't help
✅ Pros
• 100% spec-accurate decoding
• Full IE typing
• Works for NGAP/RRC/F1AP/E1AP/XnAP
• No tshark dependency
❌ Cons
• 15+ ASN.1 schema files needed
• NAS uses custom TLV — not ASN.1
• Schema version management (Rel-15/16/17)
• Very high setup complexity
Actual Results
✅ NGAP decoded perfectly from
ASN.1 PER schema
✅ RRC / F1AP / E1AP / XnAP
decodable IF schemas present
❌ NAS (TS 24.501): custom binary
TLV encoding — NOT standard
ASN.1 — needs separate parser
❌ Setup: 15+ .asn files, schema
version tracking across
3GPP Rel-15/16/17/18
Verdict: too complex for project
scope; Wireshark does this for us.

## Slide 9
Head-to-Head Comparison
Method
NAS/NGAP/RRC
F1/E1/XnAP
IE Extraction
Speed
Setup
pyshark
✅ Full
✅ Full
✅ Full
🟡 Slow
🟢 Low
scapy
❌ Raw bytes
❌ Raw bytes
❌ Manual
🟢 Fast
🟢 Low
dpkt
❌ None
❌ None
❌ None
✅ Fastest
🟢 Low
asn1tools
✅ Full
✅ Full
✅ Full
🟡 Medium
🔴 V.High
🏆 pyshark wins for 5G telecom: only method with out-of-the-box support for all 6 3GPP interfaces AND full IE extraction.
• IE = Information Element (3GPP spec-defined fields inside each message)
• Setup = effort to get the parser working with real 5G captures
• Speed measured on a 10k-packet 5G PCAP on a standard laptop

## Slide 10
Why We Chose pyshark — Decision Rationale
1
3GPP Dissectors Built-in
Wireshark's dissectors have been maintained by the 3GPP/telecom community for 20+ years. NAS/NGAP/RRC/F1AP/E1AP/XnAP all work out of the box — no custom code needed.
2
Real Field Names from the Spec
pkt.ngap.procedurecode, pkt.nas_5gs.mm.cause — exact names from 3GPP specs. scapy/dpkt give raw bytes; we'd need to re-implement the entire dissector ourselves.
3
IE Extraction Without ASN.1 Schemas
asn1tools needs 15+ .asn schema files across 6 protocols. Managing schema versions across 3GPP releases (Rel-15/16/17) would be a project in itself.
4
NAS Uses Custom Binary — Not Pure ASN.1
NAS 5GMM/5GSM messages use a 3GPP-specific TLV encoding (TS 24.007), not standard ASN.1. asn1tools can't decode it natively. pyshark handles it transparently.
5
Fallback for Synthetic PCAPs
When pyshark/tshark is unavailable (CI, containers), our raw discriminator-based fallback (scapy + single-byte protocol ID) keeps the parser functional.

## Slide 11
Live Result — What pyshark Gives Us
pyshark Parser Output (real PCAP)
Protocol : NAS (5GMM)
Procedure : NAS_Registration
Role : request
UE ID : 0x1234ABCD
IEs extracted:
• 5GMM cause = Congestion (#22)
• Registration type = Initial
• SUCI = [present]
• UE security cap = [present]
Protocol : NGAP (N2)
Procedure : InitialContextSetup
Cause IE : radio-resources-not-available
Protocol : F1AP
Procedure : UEContextSetup
Role : failure
Cause : procedure-cancelled
scapy / dpkt Output (same PCAP)
src_ip : 192.168.1.10
dst_ip : 10.0.0.1
src_port : 38412
dst_port : 38412
payload : b'\x7e\x00\x41\x00\x0a\x00...'
# That's it. Raw bytes.
# To get 'NAS_Registration' from this
# you need to:
# 1. Check byte[0] == 0x7e → NAS
# 2. Check byte[2] == 0x41 → Registration
# 3. Parse TLV IEs manually
# per TS 24.501 Table 8.2.1
# 4. Repeat for NGAP (ASN.1 PER)
# 5. Repeat for RRC (ASN.1 UNALIGNED)
# 6. Repeat for F1AP, E1AP, XnAP...
# ~3000 lines of custom code needed

## Slide 12
Summary
PCAP parsing for 5G is non-trivial
6 protocols, binary ASN.1/TLV encoding, 3GPP-specific IE structures
4 methods evaluated
pyshark · scapy · dpkt · asn1tools
pyshark selected
Only method with full out-of-the-box 3GPP dissection + IE extraction
Result on dashboard
NAS · NGAP · RRC · F1AP · E1AP · XnAP — all parsed, IEs extracted, procedures tracked, anomalies detected by 6-detector ensemble
Fallback available
Raw discriminator parsing (scapy-style) for CI/container environments
Unified Telecom Analyzer | github.com/vikasrai-tech/telecom-analyzer